## Slide 1: SISG-CFG Low Power Verification Plan
John Pratheep Kulanthai Samy

## Slide 2: Why important?
Power aware verification has become an increasingly critical issue for the semiconductor industry.
Total power consumption
Power Total = Power Dynamic + Power Static + Power Short-circuit
Static power consumption is a function of supply voltage, transistor threshold voltage and transistor size.
When operating at a higher frequency, dynamic power consumption contributes significantly to overall power consumption and is given by:
Power Dynamic = a F Cload VDD2
Notes: Shrinking process geometries have led designers to use various approaches to minimize static and dynamic power and has put immense burdens on verification teams to ensure power aware verification is complete.
Power management scheme is built by the power architect of the SoC in order to reduce the current consumption of the chip
Power Dynamic = a F Cload VDD2
Cload = Load capacitance of the CMOS
VDD = Supply voltage
F = Operating frequency at which the transition happens
a = Switching activity constant
Dynamic power dissipation is directly proportional to operating frequency and supply voltage of the devices.

## Slide 3: Clock Gating Vs Power Gating
Power gating is used for reducing LEAKAGE POWER
Clock gating is used for reducing DYNAMIC POWER
Clock Domain
- Independent of Power Domains
Voltage Domain (VDDs)
- Different voltage domains must have different clock domains.
Power Domain
- Can have 1 or more Voltage Domains and Clock Domains
Notes: Power gating is used for reducing LEAKAGE POWER by switching off power supply to the non operational power domain of the chip during certain mode of operation. Header and footer switches, isolation cells and state retention flip flips (SRFFs) are used for implementing power gating. Clock gating is used for reducing DYNAMIC POWER by controlling switching activities on the clock path. Generally Gate or Latch or FF based clock gating cells are used for implementing clock gating.
Clock domains are subset of voltage domains, i.e. NoC elements with same voltage domain may have same or different clock domains but NoC elements with different voltage domains must have different clock domains.

## Slide 4: Power Management Techniques
Power Gating
- shut down when is not active
Multi Voltage
- Multi VDDs in the design
- Multi Threshold Voltage per domain
Dynamic Voltage and Frequency Scaling (DVFS)
- change dynamically as per
the different operating modes of the design
Notes: In the DVFS technique, operating voltage, as well as the frequency, change dynamically as per the different operating modes of the design.
By varying the voltage with frequency, we can reduce the power consumption.
this technique optimizes both voltage and frequency, it is highly effective for static and dynamic power consumption.

## Slide 5: Power Management Cells
Power Switch
  Switch to OFF or ON
Isolation
  Either output ports of ON or input ports of OFF domains
  Clamp logical value to output ports of OFF domains to ON
Level Shifter
  to convert the signal from one to another voltage level (from low voltage level to high voltage level and vice versa).
Retention
  to save content of a power gated block before it switches off.
  register contains one shadow register along with the main register
Notes: This isolation cell is always a ‘power up’ cell and it prevents any unknown logic level to reach to the ‘always on’ logic.
A retention register is also needed while doing power gating to save content of a power gated block before it switches off.
The shadow register is powered by the ‘always on’ supply which stores the logic value of the block being power gated when “SAVE” is asserted high. It restores this logic value to the main register when “RESTORE” is asserted high.

## Slide 6: Multi Voltage with cell requirements

## Slide 7: UPF 2.0

## Slide 8: LP TB Block Diagram
NoC
NSPS
PMXTOR
CXT
IDI
CMI
AXI SLV
AHB SLV
CMIS SLV
S
Y
N
C
U
N
I
T
req
ack
req
ack
req
ack
ack
req
QC
I/f
rst_<pd>
host clk/rst/pwr controls
host clk/rst/pwr controls
global reset and gclocks
pwr controls
clocks
ClkGen
UFI
req
ack
APB SLV

## Slide 9: PMU/PMXTOR  NSPS

## Slide 10: PMU/PMXTOR  UPF
ns_soc_ip.v
ns_fabric.upf

## Slide 11
Refer: https://wiki.ith.intel.com/pages/viewpage.action?spaceKey=EN&title=CFG+Engineering+Home&preview=/1340616179/1545289333/CFG%20Domain%20Crossing%20Support.pptx

## Slide 13: Power Down Accept Sequence..

## Slide 14: Power Up Accept Sequence

## Slide 15: Power Down Deny Sequence

## Slide 16: Master Bridge Power Down & Up Seq

## Slide 17: Slave Bridge Power Down & Up Seq

## Slide 18: JIRA’s
•NS-40734 – Multi voltage Enable – 20Q2 - Done
•NS-40932 –UPF Power Switch with ACK ports - 20Q2 - Done
•NS-40825 - VCLP for all NoCs - 20Q2 - On going
•NS-5495 – Corekit Support in UPF - 20Q2 - On going
•NS-40460 – IDI Power on & Req -> Ack sequence - 20Q2 - On going
•NS-40892 – VCP upgrade (Service Package upgrade) - 20Q2 - Done •NS-6719 – Low Power Tracker (RBM) - 20Q3
•NS-6396 – Save/Restore (Retention) - 20Q3/4
•NS-27484 – Multi Hop (Decode Error) - 20Q4

## Slide 19: Features per Protocol
Low Power Features | IDI | CMI | UFI
Multi Clock Domain Support | YES | YES | YES
Clock Domain Crossing (Host <=> Bridges/ Within Bridges) Support | NO | NO | NO
Multi Voltage Domain Support | YES | YES | YES
Voltage Domain Crossing (Host <=> Bridges/ Within Bridges) Support | YES | NO | NO
Multi Power Domain Support | YES | YES | YES
Power Domain Crossing (Host <=> Bridges/ Within Bridges) Support | YES | YES | YES
Autowake / Decode Error Support | AUTO | AUTO | AUTO
Host and Converters are same power domain | YES | YES | YES

## Slide 20: Power simulation Tools
Static
  CLP (Cadence)
    confrml/191/19.10.300
  VCLP (Synopsys)
    vcsmx/P-2019.06-SP2
Dynamic
  Xcelium (Cadence)
    xcelium/19.03-s003
  NLP (Synopsys)
    verdi/P-2019.06-SP2

## Slide 21: Test Flow & Plan
NocWeaver,
    Generates NocStudio configs, based on Nocweaver constraint
NocStudio,
    Generates RTL & UPF, based NocStudio configs
GenStreamX
    Instantiate PMXTOR & QCD at Top
    Stitch XTORs and UPFs
    Bind checkers
Nemesis
    Generates random tests and checks
Verification & Test Plan
    SISG_CFG_Low_Power_Test_Plan.xlsx
    Located at <>/doc/internal_docs/Low_Power_Docs

## Slide 22: Where are we?
LPV
Single Voltage
PSW
DVFS
ISO
LS
Retention
Multi Voltage
UPF 2.0
Host & Bridge are same voltage domain
Autowake
Decode Error (Multi Hub)
AMBA
IDI
CMI
Static
Dynamic
CLP
VCLP
Netlist + UPF
RTL + UPF
NLP
XCE
UPF 2.1
Host & Bridge are different voltage domain
UFI
Techniques
Technologies
Standards
Stages
Features
Protocols
Power Aware
Tools