## Slide 1: Low Power Features
Clock Gating
  Fine Grained CG: Synthesis based
  Coarse Grained CG: At NoC element level
  System Level CG: External control of NoC element level clocks
Power Gating in single voltage NoC
  Power gating of individual NoC elements or group of NoC elements
Today’s focus on Power Gating

## Slide 2: NetSpeed Low Power Flow
NocStudio
Input specification contains power domains and profiles
Understands Traffic and Power profiles
Does analysis/optimization for power domains Generates low power collateral
Power Aware Design & Verif:
CPF - Power Intent
RTL with LP controls
Low Power Sequences
Assertions & Checkers
CPFs
LP aware RTL
LP Sequences
LP NoC Config
AIP

## Slide 3: A Simple NoC
H1
m0
r
s0
s1
H2
H3
PDsystem NoC Top
PD0
PD1
PD2
PPLN
PPLN
PD3
PD4
Simple 1 Master and 2 Slave Config

## Slide 4: CPF and RTL Generation
Hierarchical CPFs (v1.1) generated with COMPLETE power intent specification
Generates Hierarchical CPFs for RTL Simulation and Synthesis for RCP including voltage nets, low power libs
Isolation rules with port level information, easier for post-synthesis integration
Generates RTL for two types of low power architectures
  SW controlled power sequencing assuming external PMC
  Level-1 HW State machine assisted power sequence, reducing PMC tasks
NocStudio creates configuration registers in REGBUS layer elements and connects these to Bridges/Routers
HW State machine based sequencing is (2-3)x lower instruction count

## Slide 5: LP Sequences
NocStudio creates SW and HW power sequence generator. A PERL package invoked to generate register programming sequences for switching power profiles defined by user in NoC config
HW FSM sequencing does element level powering down in one go and polls for DONE, and hence (2-3)x faster than SW
Random stimulus generation of fine-grained power cycling of elements during AMBA traffic on/off states
Deadlock free sequences for power gate/enable operations
Power gating or enabling sequences gracefully handle transactions that are in progress or outstanding

## Slide 6: Low Power Flow: LP sequencing
H1
m0
r
s0
s1
H2
H3
PDsystem NoC Top
PD0
PD1
PD2
PPLN
PPLN
AON
RBM
RR
RM
RR
RM
REG
XTOR
PD3
PD4
Powering UP sequence order
Powering DOWN sequence order
NocPowSeq::change_power_profile(“all", “s0");
Elements to power down :
m0 r s1
Elements to power up :
None (s0 is already ON)
NocPowSeq::change_power_profile(“s0", “all");
Elements to power down :
None
Elements to power up :
s1 r m0

## Slide 7: Power Gating Sequence
CORE ID | OPERA-TION | REG NAME | ADDRESS | VALUE | RING ID | RM ID | ELEMENT ID NAME | 
0 | WRITE | PGReq | 0x80080408 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | POLL | PGRdy | 0x80081208 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | IEN | 0x80080508 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | IENR | 0x80080708 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | CKEN | 0x80080908 | 0x00000000 | 1 | 2 | 1 | m0/m
0 | WRITE | PER | 0x80080b08 | 0x00000000 | 1 | 2 | 1 | m0/m
CORE ID | OPERA-TION | REG NAME | ADDRESS | VALUE | RING ID | RM ID | ELEMENT ID NAME | 
0 | WRITE | FIR | 0x80081408 | 0x0000fd73 | 1 | 2 | 1 | m0/m
0 | POLL | FIR | 0x80081408 | 0x00000000 | 1 | 2 | 1 | m0/m
SW Register Transactions
HW FSM Register Transactions
NoCPowSeq dumps register transactions with complete details. For e.g., master bridge m0/m powering down is shown for both SW and HW FSM
HW FSM sequencing does element level powering down in one go and polls for DONE, and hence (2-3)x faster than SW
Powering down Slave bridges, for e.g., s1/s also does the same after de-mapping of it’s address range and waiting for ZERO outstanding transactions in connected master bridges

## Slide 8: Power Enable Sequence
CORE ID | OPERA-TION | REG NAME | ADDRESS | VALUE | RING ID | RM ID | ELEMENT ID NAME | 
0 | WRITE | PER | 0x80080b08 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | PDR | 0x80080d08 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | CKEN | 0x80080908 | 0x00000001 | 1 | 2 | 1 | m0/m
0 | WRITE | PGR | 0x80080408 | 0x00000000 | 1 | 2 | 1 | m0/m
0 | - | NOP |  | 100 cycles |  |  |  | 
0 | WRITE | IENR | 0x80080708 | 0x00000000 | 1 | 2 | 1 | m0/m
0 | WRITE | PDR | 0x80080d08 | 0x00000000 | 1 | 2 | 1 | m0/m
0 | WRITE | IEN | 0x80080508 | 0x00000000 | 1 | 2 | 1 | M0/m
CORE ID | OPERA-TION | REG NAME | ADDRESS | VALUE | RING ID | RM ID | ELEMENT ID NAME | 
0 | WRITE | FIR | 0x80081408 | 0x0000f171 | 1 | 2 | 1 | m0/m
0 | POLL | FIR | 0x80081408 | 0x00000000 | 1 | 2 | 1 | m0/m
0 | WRITE | PDR | 0x80080d08 | 0x00000000 | 1 | 2 | 1 | m0/m
SW register transactions
HW FSM register transactions
NocPowSeq dumping register transactions for master bridge m0/m powering up
HW FSM sequencing for power up is also (2-3)x faster than SW
Powering up slave bridges, for e.g., s1/s also does the same before mapping of it’s address range in connected master bridges
Power gate/enable sequences gracefully handle transactions that are in progress or outstanding.

## Slide 9: Assertion IP
NocStudio creates Assertion IP for LP features at various stage of collateral generation
  SW Testing: Perl based static checks generated to verify testing of configs, CPFs, RTL and Sequences. These checks are performed during collateral generation by NocStudio
  Intra element sequence Assertions: SV Assertion based checks written at per element (bridges/router) level to meet the LP functional behavior of power gating and enabling during dynamic simulations. NocStudio stitches these checks to the right LP controls of the elements
  Inter element sequence Assertions: NocStudio generates invariant SV Assertion checks to verify LP sequencing behavior of control signals across multiple NoC elements during dynamic simulations

## Slide 10: Assertion IP
  Power Profile Assertions: Stable Power profile state SV Assertion checks of NoC by parsing power intent specified from config to Power profile state switching during dynamic simulations
  Power Profile Coverage: SV property based coverage to measure the switching all power profile states and triggering of respective LP control signals. This is estimated during dynamic simulations and useful for improving LP sequencing stimulus

## Slide 11: LP Verification Tools
Static LP Verification
  Conformal LP at Pre-Sim with LEC (CLP 14.1)
  LP RCP at Pre-Synth with LEC (12.1)
  NocStudio generated collateral verification (Perl)
Dynamic LP Verification: RTL Sims verified with Incisive ncsim
  AMBA Protocol and NS checkers
  Assertion IP package excluding SW Assertions
  Simulator tool LP Assertions and Coverage

## Slide 12: Low Power Flow: LP Verification
Static LP Verification
  Conformal LP at Pre-Sim and Pre-Synth
Dynamic LP Verification: Functional LP RTL Sims verified internally with
  AMBA Protocol and NS checkers
  Bridge and Router LP functionality checkers
  NocStudio LP sequence checkers
  Power Profile switching checkers
  Simulator tool LP Assertions and Coverage

## Slide 13: 1412.1 LP Release & Status
LP Feature | 1412.1 | Comments
Single VD NoC |  | 
Conformal LP w/ LEC |  | 
CDC on LP configs |  | 
Hierarchical CPF |  | 
LP Sequences (SW & L1 HW FSM) |  | 
Power aware AMBA and NS checkers* |  | 
NocWeaver for LP configs |  | Daily 1000 configs were run with LP enabled
LP Assertion IP |  | 
SW AIP | X | 
Intra AIP |  | 
Inter AIP | X | Last minute bug in checker
PP AIP & Coverage | X | PP will become PD for v2
LP Coverage | X | 

## Slide 14: 1412.1 LP Release & Status
LP Feature | 1412.1 | Comments
Sanity TB |  | 
LP flow for Synthesis | X | Delivered to customer with flat synthesis only
Documentation |  | 
*Cold reset Power Profile | X | Due to Sanity bench support
*Clock cross to ratio fast and slow | X | Last minute RTL bug
*RTL grouping | X | 
AHBLM in same Host PD | X | Architecture bug
*Host checkers and Scbds | X | TB Transactors Sync resolves in v2
*AHB2AXI checker | X | Assertions need to be power aware
Dynamic clock frequency handling | X | TB Transactors Sync resolves in v2
Isolation and Idle value checks | X | Partially enabled, filed bugs on failing cases
* Low priority tasks (not features)

## Slide 15: Bugs found in v1 or 1412.1
Total bugs found : 63
NocStudio (7) + RTL (42) + Verif (14)
Out of 42 RTL bugs still 13 bugs are open and valid for v2
Most of the bugs are independent of v1 or v2 arch

## Slide 16: v2 Verification bench
Refer to TB Transactor Requirements document

## Slide 17: Development post 1412.1
Experiments on CPFs for Synthesis
TB Transactors requirements
Verified fixes for the open bugs in 1412.1
Power aware AHB2AXI Checker

## Slide 18: v2 LP Verif New items
LP Feature
Nemesis based on new TB Sync scheme
PMXTOR development
SYNC_UNIT development
Coverage/Test Plan
Enhanced SW AIP for LP

## Slide 20: Assumptions for v2
IEEE 1801 or UPF support ?
Single VD
Clock domain and Power domain constraints
REGBUS is not supported for Low Power