## Slide 1
Agenda
Low Power Features
Low Power Flow for Verification
Low Power Verification Tools
Dec’14 LP Release & Status
Next Steps

## Slide 2: Low Power Features
Clock Gating
  Fine Grained CG: Synthesis based
  Coarse Grained CG: At NoC element level
  System Level CG: External control of NoC element level clocks
Power Gating in single voltage NoC
  Power gating of individual NoC elements or group of NoC elements
Today’s focus on Power Gating

## Slide 3: NetSpeed Low Power Flow
NocStudio
Input specification contains power domains and profiles
Understands Traffic and Power profiles
Does analysis/optimization for power domains Generates low power collateral
Power Aware Design & Verif:
CPF - Power Intent
RTL with LP controls
Low Power Sequences
Assertions & Checkers
CPFs
LP aware RTL
LP Sequences
LP NoC Config
AIP

## Slide 4: CPF and RTL Generation
Hierarchical CPFs (v1.1) generated with COMPLETE power intent specification
Generates Hierarchical CPFs for RTL Simulation and Synthesis for RCP including voltage nets, low power libs
Isolation rules with port level information, easier for post-synthesis integration
Generates RTL for two types of low power architectures
  SW controlled power sequencing assuming external PMC
  Level-1 HW State machine assisted power sequence, reducing PMC tasks
NocStudio creates configuration registers in REGBUS layer elements and connects these to Bridges/Routers
HW State machine based sequencing is (2-3)x lower instruction count

## Slide 5: LP Sequences
NocStudio creates SW and HW power sequence generator. A PERL package invoked to generate register programming sequences for switching power profiles defined by user in NoC config
HW FSM sequencing does element level powering down in one go and polls for DONE, and hence (2-3)x faster than SW
Random stimulus generation of fine-grained power cycling of elements during AMBA traffic on/off states
Deadlock free sequences for power gate/enable operations
Power gating or enabling sequences gracefully handle transactions that are in progress or outstanding

## Slide 6: Assertion IP
NocStudio creates Assertion IP for LP features at various stage of collateral generation
  SW Testing: Perl based static checks generated to verify testing of configs, CPFs, RTL and Sequences. These checks are performed during collateral generation by NocStudio
  Intra element sequence Assertions: SV Assertion based checks written at per element (bridges/router) level to meet the LP functional behavior of power gating and enabling during dynamic simulations. NocStudio stitches these checks to the right LP controls of the elements
  Inter element sequence Assertions: NocStudio generates invariant SV Assertion checks to verify LP sequencing behavior of control signals across multiple NoC elements during dynamic simulations

## Slide 7: Assertion IP
  Power Profile Assertions: Stable Power profile state SV Assertion checks of NoC by parsing power intent specified from config to Power profile state switching during dynamic simulations
  Power Profile Coverage: SV property based coverage to measure the switching all power profile states and triggering of respective LP control signals. This is estimated during dynamic simulations and useful for improving LP sequencing stimulus

## Slide 8: LP Verification Tools
Static LP Verification
  Conformal LP at Pre-Sim with LEC (CLP 14.1)
  LP RCP at Pre-Synth with LEC (12.1)
  NocStudio generated collateral verification (Perl)
Dynamic LP Verification: RTL Sims verified with Incisive ncsim
  AMBA Protocol and NS checkers
  Assertion IP package excluding SW Assertions
  Simulator tool LP Assertions and Coverage

## Slide 9: Dec’14 LP Release & Status
LP Feature | Nov’14 | Dec’14
Single VD NoC |  | 
Conformal LP w/ LEC |  | 
Hierarchical CPF |  | 
LP Sequences (SW & L1 HW FSM) |  | 
Power aware AMBA and NS checkers |  | 
Power aware Host checkers and Scbds |  | 
NocWeaver for LP configs |  | 
LP Assertion IP |  | 
HW & NocStudio assertions |  | 
SW & Power Profile assertions |  | 
Sanity TB |  | 
Cold reset Power Profile |  | 
LP flow for Synthesis |  | 
Documentation |  | 

## Slide 10: Next Steps
Multi Voltage domain support
UPF or IEEE 1801 power format support
Re-organization of NoC for LP PnR
Low Power L2 HW FSM, higher performance than L1 HW FSM with power sequence abort support
Single Vs Multi Power domain NoC power saving analysis