## Slide 1: NetSpeed Low Power (v2) - Update LP Arch. Review and Future Direction
February 12, 2015

## Slide 2
Agenda
Overview of Low Power V2 Architecture

## Slide 3: High Level Direction
  Address issues highlighted in 1/22/15 v2 presentation
  Generally pursue v2 scheme proposed, differs in some details
  Craft HW to be flexible: where expense is not too great (area, complexity, etc.), support broader feature set.
    NocStudio policies my constrain actual implementation space.
  Support all NoCs: AMBA, streaming and Gemini
  Relax requirement to pre-define power profiles: HW allows arbitrary combinations and transitions between power states.
  Isolate NoC implementation details from PM interface
  Parity with Competition: features, area (1-2% overhead)
  State: architecture is “complete,” meaning detailed uArch and implementation planning/execution can proceed.

## Slide 4: Limitations of current low power solution
  Multi-Voltage is not supported
    Supported, details remain to be worked out, likely not phase I
  Implementation challenges (P&R and synthesis)
    Reduced (we think) – this needs ongoing attention and refinement
  Power Management(PM) control is register access only
    Signals based – simple industry standard protocol
  PM register access is RegBus based
    Regbus not required
  Slave disable (fence and drain at masters) is internally address range register based
    Automatically handled in master bridge HW on per power domain basis.

## Slide 5: Basic Architecture – 3 Layers – Simplify and Abstract NoC Power Control Details
NetSpeed Logic
PMU – (Customer Logic)
NetSpeed Power Supervisor (NSPS)
NoC

## Slide 6: PMU <-> NSPS Interface
PMU – (Customer Logic)
NetSpeed Power Supervisor
CSYSREQ_<PD>
CSYSACK_<PD>
CACTIVE_<PD>
IdleStatus_<PD>

## Slide 7: Signalling Interface - Defined
  Industry Compatible: ARM AXI™ and ACE™ Protocol Specification Section A-9: Low Power-Interface
  3 Signals (per power domain): CSYSREQ_<PD> (driven by PMU), CSYSACK_<PD> and CACTIVE_<PD> (latter 2 driven by NSPS)
    Normal Operation: CSYSREQ_<PD>, CSYSACK_<PD> and CACTIVE_<PD> all == 1
    Power Down Request: PMU drives CSYSREQ_<PD> low
      Master Bridges Fence and Drain for all targets for whom traffic flow will be interrupted
      NoC elements in requested power domain wait for idle status before acknowledging
      NSPS Acknowledges request by driving CACTIVE_<PD> low, then CSYSACK_<PD> low.
    Powered Down: CSYSREQ_<PD>, CSYSACK_<PD> and CACTIVE_<PD> all == 0
    NoC initiated wake request: Wake-on-Demand
      NoC element raises WakeReq_<PD> when it is blocked by powered down domain.
      NSPS signals wake request by driving CACTIVE_<PD> high (while CSYSACK_<PD> continuing to be held low).
    Power Up: PMU restores clock/power, then drives CSYSREQ_<PD> high.
      NSPS drives CACTIVE_<PD> high (if not already high from wake request).
      NSPS stretches ResetPwrDomain_<PD>, allows for propagation time from deassertion
      NSPS Acknowledges normal operation status by driving CSYSACK_<PD> high.

## Slide 8: Signalling interface
  Industry compatible simple IDLE/SLEEP/PowerDown req/ack based external signals per functional interface (bridges)
    Yes – industry compatible, No – per functional interface – instead per power domain
  Update internal NoC element interfaces to compatible set
    Yes
  Infer internal signals/sequences for NoC elements based on external request
    External Idle request for master i/f translates directly to idle request for master bridge
    External Idle request for slave i/f translates to slave disable from all masters and then slave idle internally
    Not per master, but NSPS Power Domain FSM translates per power domain signalling from PMU into interfaces with NoC elements that drive proper behavior (e.g., fencing and draining in masters, save entry into power down, etc.) without more detailed customer intervention.
  Define compatible states for NoC elements
    FSM implements states comparable to those listed below
    ACTIVE
    IDLE_REQ
    IDLE

## Slide 9: NSPS <-> NoC Interface – Master Bridges (per Power Domain)
NetSpeed Power Supervisor
PwrDomainActive_<PD>
FenceAck_<PD>_deasserted
Master Bridge 0
Master Bridge 1
Master Bridge 2
(note: no <PD> dependency)
FenceAck_<PD>_asserted
WakeReq_<PD>_asserted

## Slide 10: NSPS <-> NoC Interface – NoC Elements within Target Power Domain
NetSpeed Power Supervisor
SleepAck_<PD>_deasserted
All NoC Elements within Target Power Domain
SleepReq_<PD>
SleepAck_<PD>_asserted
WakeReq_<PD>_asserted
ResetPwrDomain_<PD>
NoC Elements upstream of Power Domain Boundary

## Slide 11: Features to be fixed/implemented in v2 scheme
  Implement industry compatible feature set
    Yes
  Signalling interface
    Yes
  PM control independent of RegBus
    Yes
  Slave Disable without RegBus
    Yes
  Multi-Voltage PM control
    Yes – needs more definition

## Slide 12: Industry compatible feature set
  IDLE req/ready based signalling interface
    Yes
  Key features like Power Disconnect, Wake on demand
    Yes – we support both Wake-on-Demand and Decode Error
  Clock active signalling and root level clock gating
    We deliver IdleStatus info
  Multi-Voltage support
    Yes
  DVFS
    Yes – not aware that anything defined precludes this, needs some attention.
  IP vendors are not bundling PMC in their LP solutions
    Yes – we have removed explicit instantiation of power control circuitry (e.g., power gate and isolation cell controls) – to be inserted by customer design flow, controlled by customer logic