## Slide 1: add_traffic_d Spec
Nov, 2015

## Slide 2: Traffic Specification

## Slide 3: SoC Traffic Specification with Transactions
NocStudio allows system traffic to be specified more precisely than using only point-to-point flows. The unit of traffic specification in NocStudio is a transaction, which comprises a sequence of messages between various agents of the system. A CPU may send a posted write to a memory with no response, and this simplest transaction is specified as using the notation [s m d] to indicate a message m from s to d: [cpu write mem].
Multiple messages can be joined into a single transaction. For example, a CPU may send a data load transaction comprising a load request message from the CPU to memory followed by a load data response message from memory back to the CPU: [cpu load mem],[mem data cpu]
This pattern can be extended to more steps, e.g. when there is cache controller between cpu and memory. If there is a cache miss then the transaction may involve a load request message from cpu to cache, followed by a load request message from cache to memory, followed by data response from memory to the cache, followed by data response from the cache to the cpu. This is specified as: [cpu load cache],[cache load mem],[mem data cache],[cache data cpu]
If the cache needs to perform a writeback (wb) to make room for the newly loaded data then a the cache may need to send a writeback message in parallel with the load request message to memory; such parallel messages are simply listed one after other before the next “,”. An example transaction with this parallel wb is: [cpu load cache],[cache load mem][cache wb mem],[mem data cache][mem wbresp cache],[cache data cpu]
In a coherent system, the transaction may have further complexity. For example, the cache may send a multicast snoop message to a number of other cpus. Adding this multicast message to the transaction is done by adding a multicast message specifications: {s m d1 d2 d3} indicates source s sending message m to d1, d2, and d3 and {d1 d2 d3 m s} on the next step indicates each of the destinations sending their responses back to s. The whole transaction can be specified as: [cpu load coh],{coh snoop cpu1 cpu2 cpu3}[coh load mem],{cpu1 cpu2 cpu3 data coh}[mem data coh],[coh data cpu]
In some systems, its possible that all snooped cpus will send a response message but only one of them will send actual data – this can be described by adding another data response message from snooped cpus to coh but using unicast [ ] operator instead of multicast { }, indicating a unicast response from one of the snooped cpus.
… ,{coh snoop cpu1 cpu2 cpu3}[coh load mem],{cpu1 cpu2 cpu3 resp coh}[cpu1 cpu2 cpu3 data coh][mem data coh], …

## Slide 4: Transaction vs. Flow based Traffic Specification
Attached paper: Transaction Level simulation and benefits compared to Flow level simulation
  This paper does not directly describe the traffic specification of this spec; however it describes the benefits of using multi-hop transaction specification to model NoCs in complex systems as opposed to using simple point to point connectivity based traffic.
“Transaction level simulation enables a flexible simulation infrastructure for evaluating the NoC performance at system level, This design can be easily updated and enhanced to reflect the changing system behavior and allow rapid exploration of new design choices. Together with automated NoC construction and static analysis of performance, this forms a powerful integrated platform for NoC design exploration and accurate performance evaluation vial simulation. Via evaluation on real world SoC specifications and workloads we show that transaction level specification and performance simulation can evaluate the NoC performance much more accurately and rapidly.”

## Slide 5: Grouped Transaction for Compact Traffic Specification
In complex systems with a large number of agents and complex transactions involving several messages, the total number of distinct transactions may be excessive. For example a coherent system with 16 CPUs, 16 L2 caches, 16 coherent LLCs, and 4 DRAM controllers will have 16 x 16 x 16 x 2^16 x 4 types of load transactions involving snoops and load from DRAM, that’s 1 Billion transactions. There will be several other types of transactions as well such as writeback, invalidate, load hit etc. Clearly specifying each transaction of the system is nearly impossible. To address this problem, NocStudio allows these many similar transactions to be represented by a single grouped transaction.
For example, a posted write from any of 4 cpus to any of 4 memories can be specified as: [cpu1 cpu2 cpu3 cpu4 write mem1 mem2 mem3 mem4]
In this representation, multiple transmitters and/or receivers are listed within the [ ] indicating that any of the transmitters or receivers can be chosen to send and receive this message. NocStudio also supports aliases that name a group of endpoints. By creationg the alias ‘cpus’ for all four cpus and ‘mems’ for all memories, the specification becomes: [cpus write mems]
Multihop transactions can also be specified in this way, for example: [cpus load mems],[mems data cpus]. However, when generating individual transactions from such traffic, there may be ambiguity that must be resolved based on the system behavior. The above specification could be interpreted to allow [cpu1 load mem1][mem2 data cpu3]. This sequence of messages is nonsensical in most systems, so we provide a means to control the expansion to produce only sequences of messages that are valid in the system to be modeled. First, between messages, the transmitter of a non-initial message must be on the same host as the receiver of the previous hop. This prevents a message arriving at mem1 from triggering a message from mem2.
To ensure that the initial cpu that sent the request is the cpu that the response went to, we provide transaction expansion rules to guide the expansion further.

## Slide 6: Introducing Transaction Expansion Rules
To demonstrate transaction expansion rules, consider the following snoop transaction in a coherent system:
[cpus req caches],{caches snoop cpus},{cpus snresp caches}[cpus data caches],[caches data cpus]
First, the snoop and data responses must return to the requester. This means that the cache that sent the snoops must be the one that receives the snoop response and data. Further, the cpu that initiated the request must be the one that receives the final data response from the cache.
Second, we may restrict the snoop from going to the cpu that sent the initial request, as that cpu will not have the data in its cache.
This results in valid chains of the form: cpux -> cachey -> cpuz -> cachey -> cpux, where x != z
There may be further more complex scenarios such as the cache sends an advance speculative fetch request to a memory and sends a request to an upper level cache, which finally sends request to memory to fetch data. In this case we may restrict the memory chosen during transaction expansion to be the same as the memory data comes from. Furthermore there may be cases where memory directly sends data to cpu but sends some control information to caches. In this case the caches and cpu chosen must be same. Due to such complex situations, it is non-trivial to automatically generate correct transactions from transaction group. Furthermore the rules of transaction expansion may be different based on the system design and based on the transaction context.

## Slide 7: Transaction Expansion Rules
NocStudio allows transaction expansion rules to be expressed as part of the traffic specification. Three rules are supported which can be expressed at various hops of a grouped transaction: any-to-any, same-to-same, and exclusion. The endpoint host/bridge groups of a flow group may be marked with labels to be used when selecting a host/bridge from the host/bridge groups during transaction expansion. The rules that apply to labeled endpoint groups are described below.
Any-to-Any: any endpoint from the endpoint group can be chosen during transaction expansion. This is the default behavior whenever unlabeled endpoint groups or when different labels are used in a hop, e.g.
[aliasA msg aliasB] means all of aliasA send msg to all of aliasB.
[b1 b2 msg b1 b3 b4] means b1 b2 send msg to b1, b3 and b4 (note that the b1 to b1 represents a u-turn).
Same-to-same: when a label is used multiple times, the same choice of endpoint will be made at all points that the label is used.
[1@ aliasA msg 1@ aliasA] : means a endpoint from aliasA sends msg to the same endpoint of aliasA.
[1@ cpus load mem][mem data 1@ cpus]: means that an endpoint from group cpus sends on interface load to mem and data response from mem comes back to the same endpoint.
Note that all endpoint groups that have different host groups must use different labels (which gives us a benefit that once a label is used for a transmitter or receiver bridge group, all subsequent use of the bridge groups can be replaced with just that label).
Exclusion implies that the chosen host/bridge from the alias at all places of transaction expansion where the transmitter or receiver group is marked with exclusion rule must be different. Exclusion rules are currently available only for multicast flow groups to exclude the initiating host from the multicast request message set. It is applied via multicast filters, which are described later.

## Slide 8: Using Grouped Transaction Specification
Consider a system where there are agents which
have integrated cpu, cache, mem and coherency
built into it and these agents are tiled to get scalability.
In such a system, a complex cache transaction is shown above – it uses tiles marked as A as the initiator, B as the coherency hub for the request, C as the memory controller for the address, and D and E as the tiles that get snooped. Lets assume that A, B, C, D, and E can be the same tile then it can be specified as one grouped transaction using alias all. Since any tile can be initiator we can represent A as 1@ all – we will use the label to ensure that the response comes back to the same initiator. We represent B with 2@ all, D,E with 3@ all and C with 4@ all (although we do not need a label for D and E as the normal filtering of triggered messages ensures correct expansion). We do not need to represent D and E separately instead we will use { } notation around 2@ sn 3@ all to represent sending snoops to all possible combinations of tiles. We also assume all snooped tiles sends response but one of them also sends data. The resulting grouped transaction is
[1@ all req 2@ all],[2@ sp 4@ all]{2@ sn 3@ all},{3@ snrsp 2@}[3@ data 2@],[2@ req 4@],[4@ rsp 2@][4@ data 1@],[2@ rsp 1@]
Labels are used extensively to cause the same endpoint to be used repeatedly in the expansion. This does not imply that groups with two different labels must be different; the same endpoint can be chosen for two labels during transaction expansion. In the hypothetical condition that the requester cpu cannot be snooped, an mc filter rule can be used to eliminate this overlap. (see section on multicast filter for details)
A
B
D
B
C
B
E
A
req
snoop
rsp
data
req
C
sp (speculative req)
data
rsp
rsp
A
1@
2@
4@
3@
2@
2@
1@

## Slide 9: Transaction Specification Syntax
FlowGroup (FG) represents a set of transmitting and receiving interfaces and some properties for these messages.
UnicastFlowGroup (UCFG): [txs msg rxs] represents a set of unicast flows from txs to rxs. The following syntaxes are supported for a unicast FlowGroup of a grouped transaction:
‘[‘ props [n@] host[/bridge] msg [n@] host[/bridge] ‘]’ : host indicates the host, bridge (optional) indicates which bridge of that host, msg indicates the message ‘[‘ props [n@] host/bridge.ifce “->” [n@] host/bridge.ifce ‘]’ : allows different interfaces to talk to each other
/bridge is optional for single bridge hosts, if not given the only bridge of the host is used
MCFlowGroup (MCFG): {tx msg rx} represents a set of multicast flows from each tx interface to all rx interfaces. Only syntax difference from UCFG is { } instead of [ ]. MCFGs come in pairs, in which case the first MCFG represents a multicast request, where each transmitter sends to all receivers, and the second MCFG represents the response, where each of those receivers sends its unicast response back. Additional MCFG/UCFG responses are allowed to match the MCFG request. This is useful for expressing separate MC snoop control response and MC/UC snoop data response.
FlowGroupList (FGL): One or more UnicastFlowGroups and MCFlowGroups. The FGs in the list may each be unicast or multicast. It represents parallel operations, one for each FG, such as cache sending snoops to a number of cpus (a MCFG) and also sending speculative fetch to memory controller (a UCFG). Order is not important within a FGL.
A transaction is a sequence of FlowGroupList separated by “,”. A grouped transaction’s first FGL must be a single UCFG so that this message can be put in the trace file.
Labels n@ must be followed with whitespace. The transmitters and receivers of a FG may have same or different or no label. Only one label may be applied to all transmitters of a FG and to all receivers of the FG. Furthermore when one label is applied to a transmitter group and/or a receiver group of multiple FGs, the list of hosts associated with all transmitter and/or receiver groups must be same.

## Slide 10: Transaction Specification Grammar
// by default items are whitespace separated
spec := transaction_props flow_group_list ( "," flow_group_list ) *
transaction_props := [ "-profile" ident ] [ "-rate" <0.0-1.0> ]
flow_group_list := '{' flow_group + '}' | flow_group
flow_group := unicast_flow_group | multicast_flow_group
unicast_flow_group := '[' flow_group_internal ']' // shorthand for unicast from each transmitter to each receiver
multicast_flow_group := '{' flow_group_internal '}' // shorthand for multicast from each transmitter to all receivers
flow_group_internal := endpoints [ fg_prop ] * flow_sep endpoints
fg_prop := "-dep" dep_list // specify which previous messages we need to receive before sending this message
| "-hpq_latency" int // specify host processing latency
| "-beats" int // number of beats
flow_sep := ["->" | interface_id_string ] // separate tx and rx with either -> or interface id
endpoints := label "@" endpoint + // can specify both label endpoints; must be consistent with other uses of label
| label "@" // endpoint is optional when label has been used before
| endpoint + // label is not optional
endpoint := bridge | host | interface // can omit bridge if host has only one bridge, can omit interface if message_type is specified in flow_sep
interface := bridge "." interface_id_string
bridge := host "/" ident
host := ident
label := int
dep_list := dep | multi_dep
multi_dep: '{' dep + '}'
dep := [int':']int // first int is optional. If not specified, it is assumed that dep is to flow group on the preceding hop.
interface_id_string := ? "ar" | "aww" | ... ?
ident := ? [ 'a'-'z' | '_'] + ?
int := ? integer ?
Semantic requirements:
First flow_group_list must have single element (can't have multiple messages that start transaction)
Each flow_group not in the first flow_group_list must have its transmit endpoints match hosts with receive endpoints of some flow_group in the previous flow_group_list (must be triggered by some previous message)
  receive endpoints do not need to match tx endpoints on next hop

## Slide 12: Connectivity between Consecutive FlowGroupLists
[A -> B] , [B -> C] , {DE -> B} , [B -> C] -> [C -> B] , [B -> A]
{B -> DE} [DE -> B] [C -> A]
Connectivity between tx and rx endpoints of a flowgroup (FG) is any-to-any (adhering to the transaction expansion rules). However connectivity between rx endpoints of a flowgrouplist (FGL) and tx endpoints of the next FGL of a groups transaction is not any-to-any - its one-to-one based on the order of the endpoints present in each FG. The n-th rx endpoint of a next FGL can only trigger a message to be sent from the n-th tx interface of a previous FG. As a result, the number of tx endpoints as well as the order of their hosts of each FG of a non-first FGL must match the number of rx endpoints and order of their hosts of at least one FG of the previous FGL. Multiple matches – a FG of a next FGL matching multiple FGs of the previous FGL – are allowed, which indicates that multiple messages must be received before the next message(s) of the FG can be sent. If the FG rx hosts of a FGL does not match the FG tx hosts of any FG in the next FGL, then that message will not trigger any further messages, and that branch of the message sequence will terminate. Consider the following example:
A
B
D
B
C
B
E
A
req
snoop
rsp
data
req
C
sp (speculative req)
data
rsp
rsp
A
Here the second FGL’s FG B > C terminates as its tx host group (C) does not match any rx host groups (DE) of any FGs of the third FGL.
The third FGL contains a response MCFG and a UCFG, both matching the previous request MCFG, indicating that all DEs send response but one DE also sends data.
The fourth FGL’s FG’s tx host group matches two rx host groups of the third FGL. This causes the fourth FGL’s message to be sent after the arrival of both messages. During multiple matches, the exact connectivity may be specified at each next FGT’s FG by adding a –dep flag.
Indicates that first B-C msg
terminates upon arrival at C
Indicates that second B->C msg is sent upon arrival of all {DE->B} msgs and [DE->B] msg
All -dep values must point to a valid FG in the previous FGL.
A -dep value may only point to those FGs of the previous FGL, which have a matching host group (identical hosts in the same order).

## Slide 13: Connectivity between Consecutive FlowGroupLists
Here is a visual representation of the requirements between consecutive FGLs and how the FG connectivity is different from the connectivity within a FlowGroup. The colored circles represent interfaces and color represents the host of the interface; circles of same color may or may not be identical interfaces. Note that the order of interfaces within a FlowGroup matters, but the order of the FlowGroups in the FlowGroupList does not matter.
[ ] UCFG
{ } MCFG
X Terminate
X
MCFG
request
MCFG
response1
MCFG
response2

## Slide 14: Examples of Illegal and Legal Grouped Transactions
Illegal because a grouped transaction have a MCFG in the first FGL. First FGL may have one UCFG only
X
Illegal because a MCFG in a FGL must be followed up with another MCFG at the next FGL
Illegal because the MCFG in the second and third FGL do not have matching hosts in the same order
Legal transaction; green line indicates the connection between FGs of the consecutive FGLs. O indicates parallel multicast messages.
Illegal because MCFG in third FGL cannot match with UCFG of the second FGL. Even if we make the second UCFG MCFG, their transaction expansion labels are different. Rx of request and tx of response MCFGs must have same rule.
1@
2@
Illegal because same expansion rule label is used at different host/bridge group. Different host/bridge groups must use different labels.
1@
1@
1@
2@
-dep 1,2
Illegal because in the “–dep 1,2” 2 refers to a non-matching FG of previous FGL. -dep must point to matching FG positions in previous FGL. Also 1@ and 2@ of the MCFG request and response is wrong same host groups must use same label (in this case it means host receiving MC response can be different from the host sending request)

## Slide 15: MCFG Transport
X
Different fabrics and endpoints may have different capabilities when it comes to multicast. Different levels include:
  Full multicast support: any message can be sent to a any collection of destinations
  Limited multicast support: only some requests can be multicast or only some destination patterns are supported
  No multicast support: multicast is emulated by sending multiple unicast messages
Based on the level of support in the transmitter and the fabric, an MCFG can be sent in the most efficient method available to both.
The mode of transport is not a property of the transaction

## Slide 16: Multicast Filters for Smart Snoops (1/4)
Multicast filters are used to control number of messages sent as part of a MCFG – based on the filter a subset of messages from the MCFG request and response are sent. The rule is applied during simulation after individual transactions are created from grouped transactions. It can be used to control the MCFG-specified snoops. The multicast filter determines:
- Number of agents and which agents to which send the MCFG request (can be used to control snoop requests)
- Which agent returns the unicast MCFG response, if specified with MCFG responses (can be used to control which agent sends data)
- Whether to send MCFG message to the transaction initiating agent or not (can be used to allow snooping of the initiating agent)
To create a filter, the command syntax is:
add_mc_filter <filter_name> \
<-ifce_id <if id>> -num_mcfg_targets n1:w1 n2:w2 n3:w3 … nm:wm \
-host_mcfg_target_weights h1:wq1 h2:wq2 h3:wq3 … hm:wqm \
-host_unicast_resp_weights h1:wr1 h2:wr2 h3:wr3 ... hm:wrm \
–omit_initiator wm is the probability of sending MCFG requests to nm hosts; and wqm is the probability that host hm is selected; wrm is the probability of host hm getting selected for the Unicast response of MCFG request.

## Slide 17: Multicast Filters for Smart Snoops (2/4)
The –host_mcfg_target_weights and the –host_unicast_resp_weights are optional arguments, which when not specified will assign equal weights to all the hosts in the NoC.
Both the arguments accept weight assignments on individual hosts or aliases or * (for all hosts).
However the command will error if it attempts to assign weight only to hosts that have already had their weights assigned before.
The weights are assigned to the hosts/alias from left to right in the order in which they appear in the argument.
  $ add_alias host_alias h1 h2 h3
  $ host_mcfg_target_weights h1:0.25 host_alias:0.5
In this example, h1 is assigned 0.25 and h2 and h3 are assigned weights 0.5 .
$ host_mcfg_target_weights h1:0.25 h2:0.25 h3:0.25 host_alias:0.5
This will result in an error as host_alias does not assign weight to any new/unassigned host.
$ host_mcfg_target_weights host_alias:0.25 h2:0.25
This will result in an error as it attempts to re-assign weight to h2.
$ host_mcfg_target_weights h1:0.25 host_alias:0.5 *:0.75
This will assign 0.25 to h1, 0.5 to h2 and h3 and assign 0.75 to all other hosts. If there are no other hosts, then it will error out as the *:0.75 does not assign weights to any new unassigned hosts.

## Slide 18: Multicast Filters for Smart Snoops (3/4)
After a multicast filter has been created, it can be applied to a combination of transactions, profiles and hosts as follows:
apply_filter <filter_name> [-host <host_name>] [-profile <profile_name>]
[-transaction <transaction_name/key>]
If a host, profile or transaction is not specified, then the filter gets applied over all objects of that type.
When a multicast filter is applied on a transaction, NocStudio first chooses how many hosts to which the MCFG request is sent, then it chooses so many target hosts from among the list of all targets specified in the MCFG and based on the weights of each target, and finally it chooses which target returns unicast response (if it is specified).

## Slide 19: Multicast Filters for Smart Snoops (4/4)
Here is an Example
In this example, the add_traffic_d command is used to construct a transaction in which host A (CPU) sends a request to host B (CCC), snoops the CPUs C,D,E,F and returns the snooped data to A.
The multicast filter mc_filter is defined to choose 1 or 2 or 3 or 4 MCFG groups (snoop targets) probability 75%, 10%, 10% and 5%, respectively. Each of the hosts C,D,E,F is equally likely to be snooped because their weights are all 0.25. Further, each is equally likely to respond with data. The requester is not snooped by the CCC. The figure shows what happens when the filter snoops two targets, and picks hosts D & E to snoop. Among the snooped targets, D is chosen to respond with the data.
This filter is applied to the transaction using the apply_filter command, which by default applies this filter to all the hosts, profiles and transactions in the system.
A
B
D
B
A
req
snoop
Snoop rsp
C
E
F
Snoop rsp
Data
rsp
$ add_traffic_d [A req B],{B snoop C D E F},{C D E F snoop_rsp B}[C D E F data B],[B rsp A]
$ add_mc_filter mc_filter \
-num_mcfg_targets 1:0.75 2:0.10 3:0.10 4:0.05 \
-host_mcfg_target_weights C:0.25 D:0.25 E:0.25 F:0.25 \
-host_unicast_resp_weights C:0.25 D:0.25 E:0.25 F:0.25 \
–omit_initiator
$ apply_filter mc_filter

## Slide 20: U-Turns in NoC (1/2)
In the context of NoC, U-turns refer to a traffic flow with the Transmitting and Receiving Interfaces on the same bridge (of the same host).
U-turns are allowed on all hops of the transaction except for the first. The U-Turns are dealt within the host, without the packets getting ejected into the NoC.
For example,
$ add_traffic_d -rate 0.2 [ A/p1 a B/p1 ] , [ B/p1.c -> B/p1.d ] , [ B/p1.b -> A/p1.b ]
In this transaction, the second hop involves the packets being transmitted from and received at the same bridge h2/p1. These packets will not be ejected onto the NoC, but rather be transmitted and received internally within the host without entering the NoC.
A
B
A
a
b
c/d

## Slide 21: U-Turns in NoC (2/2)
In this example,
$ add_alias host_alias h1 h2
$ add_traffic_d -rate 0.2 [ 1@ host_alias a 2@ host_alias ] , [ 2@ host_alias b 3@ host_alias ]
In this example, a group of hosts h1 and h2 are represented using their alias host_alias. There will be 4 chains generated as uturns are not allowed on the first hop.
        h1/p1 -> h2/p1 -> h1/p1
        h1/p1 -> h2/p1 -> h2/p1
        h2/p1 -> h1/p1 -> h1/p1
        h2/p1 -> h1/p1 -> h2/p1
The chains :
        5. h1/p1 -> h1/p1 -> h1/p1
        6. h1/p1 -> h1/p1 -> h2/p1
        h2/p1 -> h2/p1 -> h1/p1
        h2/p1 -> h2/p1 -> h2/p1 will not be generated as u-turns are not permitted on the first hop.

## Slide 22: Grouped Transaction Correctness Requirements
A grouped transaction’s first FGL must be one UCFG only; neither multiple UCFGs nor MCFG are allowed at the first hop FGL.
A MCFG must be followed by a matching MCFG, first indicating the MC request and second a MC response. A MCFG request may have additional MCFG or UCFG responses.
The number of tx interfaces as well as the order of the hosts of each FG of a next (non-first) FGL must match the number of rx interfaces and order of their hosts of at least one FG of the previous FGL. Multiple matches – a FG of a next FGL matching multiple FGs of the previous FGL – are allowed, which indicates that each rx message, corresponding to every match must be received before next message(s) of the FG can be sent.
If a FG rx hosts of a previous FGL does not match any FG tx hosts of next FGL, then the previous FG branch of the transaction terminates once its rx msg(s) are received.
In a grouped transaction, all transmitter and receiver groups that have different hosts must use different or no label.
All -dep values given must point to a valid FG in the previous FGL (starting from index 0 indicating the first FG).
All -dep values must point to those FGs of the previous FGL, which have a matching host group (identical hosts in the same order).

## Slide 23: Traffic Command - add_traffic_d
add_traffic_d trans_props <'[' | '{'> <h/p> <msg> flow_group_props <h/p> <']' | '}'> + \
[, <'[' | '{'> <h/p> <msg> flow_group_props <h/p> <']' | '}'> + ]*
trans_props is [-profile <names>] [-rate <value>]
flow_group_props is [-beats <value>] [-hpq_latency <value>] [-deps <fg_indices>]
Adds the traffic sequence between a series of host bridge names or aliases. Properties of the traffic can be average rate (bw), peak rate (peak), latency, host processing latency and number of beats.
Detailed description:
Adds the traffic transaction (sequence of message{s}) between a series of single or multiple interfaces. Traffic specification supports the use of host and/or bridge aliases. Aliases are expanded by NocStudio when the command is parsed.
The user can specify certain transaction properties at the beginning of the traffic command.
  [profile] - The profile(s) specifies to what traffic profile(s) this transaction belongs. A collection of profiles may also be specified in which case the transaction would belong to each of them. A collection must start with "{" and end with "}" and contain valid profiles, e.g. {prof1 prof2} or {prof4 prof7 prof9}. Default profile is system.
  [rate] - is the average message transmission rate, specified as float from 0 to 1, with 1 meaning sending every cycle and 0.1 meaning sending one response every 10 cycles. Default value is 0.1.
The traffic transaction are specified as a series of hops. Each hop can be specified as a list of one or more flow groups (FG). A FG is essentially message(s) between one or more transmitting interfaces and one or more receiving interfaces. A unicast message is enclosed in “[“ and “]” while a multicast message is enclosed in “{“ and “}”. Multiple FGs within a hop are white-space separated and indicates that the FGs operate in parallel. Different hops of a transaction are separated by a comma ‘,’.
In the flow group specification, a set of parameters specific to that flow group can be specified.
  [beats] - is the number of beats in the FG’s messages at the transmitter; is used for link analysis and optimization. Default is -1 indicating that the interface properties are used to compute this value.
  [noc_latency] - is the required latency for the flow group message in nanoseconds. Default is -1 indicating no latency constraint.
  [hpq_latency] - is the latency of the packet before being transmitted in tx bridge's host_clock_domain clock cycles. Default is -1 indicating no additional latency during packet transmission.
  [deps] - is the list of all flow group indices in the flow groups (FG) of previous flow group lists (FGL). Specifying a dep indicates a dependency between the rx interfaces of a previous FGL that the transmitting interface of the current FG – when messages on all rx interfaces are received, the messages of this FG can be transmitted. The syntax for specifying a dep is FGL_id:FG_id where FGL_id is the flow group list ID starting from 0 and FG_id is the flow group ID in the specified FGL starting from 0. The FGL ID is optional. If it is not specified, it is assumed that the dep originates from a FG on the preceding FGL. By default when no deps are specified, all FGs of the preceding FGL whose hosts of the rx interfaces match the current FGs tx hosts by order, has a dependency on the current FG. A set of deps must start with { and end with } and are space separated.
  .

## Slide 24: Chain Explosion Problem
When a multi-hop grouped transaction is specified for a large number of host/bridge groups then the total number of transactions generated during expansion can be excessive. To address this problem, NocStudio performance simulator never expands a grouped transaction into all of its individual transactions. Instead, a transaction is drawn uniformly randomly from the grouped transaction every time an initiator (first tx interface of the transaction) attempts to initiate the grouped transaction.
When there are multiple grouped transactions specified at an initiating tx interface, one of the grouped transaction is first chosen. This selection is based upon the rate of the transaction and the simulation mode.
The simulation results are stored for those expanded transactions that are actually simulated during the simulation.

## Slide 25: More Complex Examples of Grouped Transactions
X
add_traffic_d -profile profile0 -rate 0.2 [h0/p0 a -> h1/p1] , [h1/p1 a -> h2/p2] , [h2/p2 b -> h1/p1], [h1/p1 b -> h0/p0]
  This adds a multi-hop transaction from bridge h0/0 to bridge h1/p1 which in turn transmits to h2/p2. h2/p2 the responds to h1/p1 and h1/p1 then responds to h0/p0. Profile "profile0" is specified and the specified rate is 0.2.
add_traffic_d -profile profile1 -rate 0.2 [h0/p0.a -> h1/p1.a] , {h1/p1.a -> h2/p2.a h3/p3.a} , {h2/p2.b h3/p3.b -> h1/p1.b}, [h1/p1.b -> h0/p0.b]
  This adds a multi-hop transaction from bridge h0/0 to bridge h1/p1 which in turn sends a multicast message to h2/p2 and h3/p3. h2/p2 and h3/p3 then send a multicast response to h1/p1 and h1/p1 then responds to h0/p0. Profile "profile1" is specified and the specified rate is 0.2.
add_traffic_d -profile profile1 -rate 0.2 [h0/p0.a -> h1/p1.a] , {h1/p1.a -> h2/p2.a h3/p3.a} , {h2/p2.b h3/p3.b -> h1/p1.b} [h2/p2.c h3/p3.c -> h1/p1.b], [h1/p1.b -> h0/p0.b]
  This adds a multi-hop transaction from bridge h0/0 to bridge h1/p1 which in turn sends a multicast message to h2/p2 and h3/p3 (possibly a snoop). h2/p2 and h3/p3 then send a multicast response to h1/p1 (possibly a snoop response). In parallel, either h2/p2 or h3/p3 will also send a message to h1/p1 (possibly data response). h1/p1 then responds to h0/p0. Profile "profile1" is specified and the specified rate is 0.2.
add_traffic_d -profile profile1 -rate 0.2 [h0/p0 a -> h1/p1] , [h1/p1 a -> h2/p2] [h1/p1 a -> h3/p3] , [h2/p2 b -> h1/p1] , [h1/p1 b -> h0/p0]
  This adds a multi-hop transaction from bridge h0/0 to bridge h1/p1 which in turn sends parallel messages to to h2/p2 and h3/p3. However only h2/p2 sends a response to h1/p1. The message to h3/p3 terminates. h1/p1 then responds to h0/p0. Profile "profile1" is specified and the specified rate is 0.2.
add_traffic_d -profile profile1 -rate 0.2 [h0/p0 a -> h1/p1] , [h1/p1 a -> h2/p2] [h1/p1 b -> h2/p2] , [h2/p2 c -deps 1:0 -> h3/p3] , [h3/p3 b -> h0/p0]
  This adds a multi-hop transaction from bridge h0/0 to bridge h1/p1 which in turn sends parallel messages to to h2/p2. However h2/p2 only depends on the tx message from h1/p1 to h2/p2 on interface 'a' to beging transmitting to h3. h3/p1 then responds to h0/p0. Profile "profile1" is specified and the specified rate is 0.2.