## Slide 1: NetSpeed Orion Low Power (v2) LP Arch. Review and Future Direction
January 22nd , 2015

## Slide 2
Agenda
Limitations of current scheme
v2 scheme

## Slide 3: Limitations of current low power solution
  Multi-Voltage is not supported
  Implementation challenges (P&R and synthesis)
  Power Management(PM) control is register access only
  PM register access is RegBus based
  Slave disable (fence and drain at masters) is internally address range register based

## Slide 4: Blocks/impediments for Multi Voltage Support
  RegBus assumes/requires
    Single Clock
    Single Power Domain
    Single Voltage Domain
  PM control (including L1 FSM) sits in RegBus power domain
  Clock domain definitions
    All elements at given node are constrained to same noc-clk
    RegBus ring assumes single noc-clk for complete ring at the node

## Slide 5: Implementation Challenges (Synthesis and P&R)
  Current scheme assumes un-gated active logic in power gated partitions
    Need custom cells
    Or need power delivery design flow to create exceptions in voltage islands
  Issues with Isolation-cell placement at hierarchical synthesis
  Issues with DFT insertion
    Missing Isolation-cells

## Slide 6: PM control is register based and RegBus based
  Slow
  Expensive
  Serial
  Assumes AON available throughout the chip
  Assumes at-least one CPU core and associated sub-system always up before waking NoC elements

## Slide 7
Agenda
Limitations of current scheme
v2 scheme

## Slide 8: Features to be fixed/implemented in v2 scheme
  Implement industry compatible feature set
  Signalling interface
  PM control independent of RegBus
  Slave Disable without RegBus
  Multi-Voltage PM control

## Slide 9: Industry compatible feature set
  IDLE req/ready based signalling interface
  Key features like Power Disconnect, Wake on demand
  Clock active signalling and root level clock gating
  Multi-Voltage support
  DVFS
  IP vendors are not bundling PMC in their LP solutions

## Slide 10: Signalling interface
  Industry compatible simple IDLE/SLEEP/PowerDown req/ack based external signals per functional interface (bridges)
  Update internal NoC element internal pm interfaces to compatible set
  Infer internal signals/sequences for NoC elements based on external request
    External Idle request for master i/f translates directly to idle request for master bridge
    External Idle request for slave i/f translates to slave disable from all masters and then slave idle internally
  Define compatible states for NoC elements
    ACTIVE
    IDLE_REQ
    IDLE

## Slide 11: Slave Disable (Without RegBus)
  Ability to disconnect/disable slave bridges depend on masters fencing the requests for the slave bridges
  Disabling slave bridges without request fence can stall the complete NoC
  Need to implement a non-RegBus solution
  Master bridge update required
  Option 1 : Use sideband signalling between PM control logic of slaves and Master bridges
    Becomes non-trivial for async and multi-voltage
    Could add multiple sidebands and their routing pipelines
  Option 2 : Use a scheme where map states are maintained in Master and Slave bridges
    Map state updates can be done using special commands sent over normal NoC layers
    In-band messaging scheme has to be dead-lock free
    Additional logic to generate and intercept the packets would cost area in bridges.
    No internal sidebands required
Notes: Current scheme
- Reg bus access based
- Needs demap/poll of registers in all master bridges
Limitations
- Needs RegBus
- Slow, serial, expensive
- Needs micro-sequencer to enable a signalling interface.

## Slide 12: Power Disconnect and Auto-Wake
  Ability of master or slave at an interface to independently ask for dis-connect
  Prevent initiation new request (Fence)
  Graceful handling of pending request (Drain)
  Define alternate behaviour for request in disconnected state
  Configurable feature to generate wake request if new request are received in disconnect state

## Slide 13: Multi-Voltage PM control
  Decouple PM control logic from RegBus
  Implement required common PM control logic (used for sequencing and inferred transitions) per power domain
  New NoC elements dedicated to be used for ASYNC transfer across voltage domains
  NoC studio updates e.g.
    Define Voltage domains in consistent manner
    Account for async cross-overs at voltage domain crossing

## Slide 14: ORION Low-Power v2 Option 1
  Fix Slave Disable
  Re-organize L1 FSM and implement L2
    Provide signalling interface
    Implement logic to mimic features like power disconnect, auto wake etc
  Find alternate to RegBus layer for L1 and L2 programming
  Implement sideband communication that can work across voltage domains for communication among L1 and L2 fsm

## Slide 15: ORION Low-Power v2 Option 2
  Fix Slave Disable
  Implement signalling interface
  Scrub the logic to retain only minimal functions expected from NoC IP
  Remove SoC Power Management Unit features from NoC IP (isolation control, power enable etc)
  Implement small pm controllers for managing state transitions, sequencing, auto-wake etc
  Keep state definition simple to be captured by the signal state at interface
    Even pm control can move to gated domain if Auto-Wake is not required (state captured by isolation value)
  Optionally implement L2 sequencer
    Provide register based control at higher abstraction level (Power Profile switch, commit/abort operations etc)