## Slide 1: NetSpeed Orion Low Power Product Overview Meeting
May 20, 2015

## Slide 2: Introduction
NetSpeed Orion supports an extensive set of low power features: clock gating, power gating, and multiple voltage domains
Highly automated: power intent is specified in NocStudio configuration file, low power solution generated automatically
Simple, industry standard power control interface: AMBA Low Power Signaling Interface – Q-channel
NetSpeed Power Supervisor implements a simple state machine to coordinate power sequencing activity among all NoC elements
  Fencing and Draining
  Auto-Wake-Up
  Sleep Request/Sleep Acknowledge (idle state detection and confirmation)
Simulation and synthesis supported by automatically generated CPF/UPF files

## Slide 3: Basic Architecture – 3 Layers – Simplify and Abstract NoC Power Control Details
NetSpeed Logic
PMU – (SoC Power Control)
NetSpeed Power Supervisor (NSPS)
NoC
Q-Channel (1 channel per power domain)
Internal NoC Power Control

## Slide 4: PMU (SoC Power Control) Interface
  AMBA Q-Channel Signaling Interface: 4 signals – QREQn, QACCEPTn, QDENY, QACTIVE
  ResetPwrDomain_n: per domain reset under PMU control
  Power Controls: Integrated via UPF/CPF – isolation, power gating, clock gating enables, level shifters
PMU – (SoC Power Control)
NetSpeed Power Supervisor
QREQn_<PD>
QACCEPTn_<PD>
QACTIVE_<PD>
QDENY_<PD>
reset_pd_n_<PD>
Isolation, PG, CG enables (via UPF/CPF)
NetSpeed NoC

## Slide 5: PMU Signalling – Power Down Sequence

## Slide 6: PMU Signalling – Power Up Sequence w/Auto-Wake Request

## Slide 7: NetSpeed Low Power Flow
NocStudio
Input specification contains power domains and profiles
Understands Traffic and Power profiles
Does analysis/optimization for power domains
Generates low power collateral
Power Aware Design & Verif:
UPF/CPF - Power Intent
RTL with LP controls
Assertions & Checkers
UPF/CPFs
LP aware RTL
LP NoC Config
AIP

## Slide 8: NetSpeed Solution Simplifies the Power Management Problem
NocStudio intelligence and algorithms applied to PM
  NocStudio Traffic Profiles specify communication patterns
  NocStudio Power Profiles specify power domains that are active
  In a given Power Profile, NocStudio knows the NoC elements / domains it does not need ON
Power Management using NocStudio
  Tune-power efficiently assigns NoC routers to power domains to…
    Minimize leakage power
    Minimize physical design complexity
    Minimize traffic interdependencies and disruptions

## Slide 9: Tune Power
NocStudio creates routers while synthesizing the network
‘Tune power’ is a NocStudio optimization which auto assigns power domains to routers
Auto-assignment is based on adjacency, hardware cost, and on required traffic flows
Tune
power

## Slide 10: Example: A Simple NoC with Power Management
Simple 1 Master and 2 Slave Config
m0
s0
PD1
H2
PD0
H1
r
PD4
PD2
PD3
s1
H3
PPLN
PPLN
NSPS
PDsystem

## Slide 11: Low Power Flow: Power Intent Spec in Config
new_mesh 4 4 1 lp_example regbus_enabled
mesh_prop low_power_enabled yes
add_power_domain PD0
add_power_domain PD1
add_power_domain PD2
add_power_domain PD3
add_power_domain PD4
add_host m0 …….
add_traffic ………
add_range ………
bridge_prop m0/m power_domain PD0
bridge_prop m0/m power_domain_host PD4
bridge_prop s0/s power_domain PD1
bridge_prop s0/s power_domain_host PD1
bridge_prop s1/s power_domain PD2
bridge_prop s1/s power_domain_host PD3
add_power_profile m0_s0 PD0@ON PD1@ON PD4@ON
add_power_profile m0_s1 PD0@ON PD2@ON PD3@ON PD4@ON
add_power_profile s0_s1 PD0@ON PD1@ON PD2@ON PD3@ON
map
tune_power 1 1
gen_ip
Low power features enabled.
Creates new power domains for NoC elements.
Assign created power domains to NoC bridges. Host power domain can be set same as bridge.
Creates power mode conditions or power state tables. Only bridge power profiles are added.
Assigns power domains to routers and links based on the power profile info.

## Slide 12: UPF/CPF Generation
Hierarchical CPF/UPFs generated with power intent specification for
  Pre-Simulation for RTL simulations and
  Pre-Synthesis including voltage nets, low power libs
Isolation rules with port level information, easier for post-synthesis integration
Testbench CPF/UPF for modeling host interface power domains (for Sanity bench)