## Slide 1: NetSpeed Orion Trace & Debug Feature Set Overview
March 18, 2016

## Slide 2: Introduction
NetSpeed Orion implements rich trace and debug functionality supporting the following features
  Error and statistics monitoring in NoC elements with maskable interrupt generation
  Non-invasive tracing of network interfaces
  Coresight compliance
  Low power: support for debug across power and clock domains, may be powered down when not in use.

## Slide 3: Architectural Overview
NetSpeed Logic
DAP
APB-AP
NS Regbus Master
APB
Regbus
NS NoC
NS AXI4 Master Bridge
Regbus
AXI
Trace
NS Trace Slave
ATB
Trace
TPIU
ATB
Interrupt
Monitor/Capture
NS Trace
Master

## Slide 4: Architectural Overview (continued)
Regbus: dedicated control layer in the NoC, isolated from other traffic, accessed via NS Regbus Master (AXI4 interface).
Debug Access: provided via alternative APB interface to Regbus Master, which bridges the debug APB interface to NS Regbus to access configuration registers.
  Coresight Reusable Component register interfaces implemented.
  Monitor/Capture and Trace Bridge components may alternatively be directly connected to debug APB.
Error status (and general status), interrupt and statistics controls accessible via Regbus, with debug visibility via debug APB.
Packet trace data transported through NoC on isolated layer to NS Trace Slave, which bridges and funnels trace data into one or more ATB interfaces.
  Trace data may alternatively be driven directly into a separate ATB network.

## Slide 5: Error and Statistics Monitors/Interrupts
Initiators
  Transaction Errors: captured (address and error code), maskable interrupt generated.
    Separate/Parallel monitors for read and write channels.
  Timeout: interrupt when transaction response latency exceeds configurable threshold.
  Statistics: Address/Command match registers drive counters measuring packet counts and response latencies.
  AID Table Status
Targets
  Transaction Errors: captured (address and error code), maskable interrupt generated.
    Separate/Parallel monitors for read and write channels.
NoC Routers
  Error Conditions: maskable interrupt generated (e.g., blocked interface)
  Status and Statistics: FIFO status, programmable event counters

## Slide 6: Packet Tracing
Coresight Reusable Component implementing non-invasive monitoring of network interface at either initiator or target (or both)
Filtering and Event/Trigger Generation: events may be combined via Boolean functions and used to generate derived events
  Address Comparitors
    Initiator: leverage address map logic for address range events
    Initiator/Target: optional configurable address & address range match registers
  Control Comparitors: set of configurable control field registers
  Error Status
  Counters
  Sequencer
  External trigger inputs, event outputs (CTI)
ATB compatible trace output: transported through NoC to NS Trace Slave.
  Selectable Output: any or all of Address, Auxillary, and Data

## Slide 7: Additional Features
Domain Specific Monitoring/Capture: e.g., Coherency – Gemini CCC Tracing Module.
Fencing/Draining Control: debug APB to Regbus master provides interface to NS Power Supervisor logic to allow isolation of NoC access to specific components of interest.
  Peripherals can be held off on clean transaction boundaries to allow exclusive NoC access to subset of design under active debug.

## Slide 8: Technical Requirements
Enhancement to Regbus Master (RBM) to support an Debug APB interface, perhaps in parallel with AXI-like interface
  Locally implement Coresight compliant register table to support interface with power supervisor to implement debug control of power, clock gating and fencing/draining.
  May want RB Tunnel to have mode to operate with APB semantics
  Implement a simple 32 to 64-bit data width translation scheme on APB interface, perhaps with per source identification to maintain multiple of these resources in parallel
    Writes: to upper address first, cached in RBM, commit 64-bits upon write to lower address.
    Reads: first read to upper/lower address returns appropriate data, caches other half. Subsequent read to other have with no intervening reads returns cached copy.
Probe/tracing logic for master and slave bridges: writes data to dedicated NoC port in proprietary format. Supports Coresight compliant register interface and related features.

## Slide 9: Technical Requirements (continued)
Trace Target Slave: slave port on NoC that accepts proprietary trace format and bridges to 1 or more ATB interfaces, performing Coresight funnel function in the process.
NocStudio
  Map trace data onto dedicated physical layer
  Instantiate probe bridges next to (on same node as) normal bridges and connect them to trace data layer
  Instantiate trace target bridges on trace data layer
  Support RBM/Tunnel enhancements

## Slide 10: Future considerations
Sharing probe/tracing resources across bridges… perhaps bridges aggregated at single node (connecting to multiple associated router ports) could share probe/tracing interface to reduce overhead (this seems to be implied by Intel XG631 spec).
Probing/tracing at router interface: point of aggregation, gain insight into network traffic flow…
Do we need to implement an APB master bridge for our NoC to allow it to carry Coresight debug APB to non-NoC components?
Do we need to implement ATB master/slave bridges to allow NoC to transport trace info from other components?
Should we be trying to merge trace data layer with regbus layer? Should we have the option of carrying either/both on normal layers? Both represent trade-offs of expense vs. invasiveness).

## Slide 11: Error and Statistics Monitors/Interrupts - Backup
Initiator Error Mask
  e0 - Local read address decode error: ARADDR did not find a match in the master bridges address table and a decode error was issued.
  e1 - Read address decode error from slave: A decode error response was received from a slave device.
  e2 - Read slave error: A slave error response was received from a slave device.
  e3 - Non modifiable WRAP: A WRAP command marked as non-modifiable (ARCACHE[0]=0) was detected.
  e4 - Fixed transaction detected: An AR command of FIXED burst type was detected.
  e5 - Read address multi-hit: An AR command matched against multiple entries in the address table.
  e6 - Read response timeout: Read response timeout occurred. With timeout enabled, a response wasn't received within the expected interval.
  e7 - Read WRAP not equal to 64B cacheline size: A WRAP command not equal to cache line size of 64 Bytes was detected.
  e16 - Local write address decode error
  e17 - Write address decode error from slave
  e18 - Write slave error
  e19 - Non modifiable WRAP
  e20 - Fixed transaction detected
  e21 - Write address multi-hit
  e22 - Write respone timeout
  e23 - Write WRAP not equal to 64B cacheline size
  e32 - capture counter0 overflow
  e33 - capture counter1 overflow
  e34 - traffic sent to a noc layer which is power gated